Note to users: items shown in red indicated edits / selections that need to be made to tailor the specification for the application.

Metraflex Modular Riser Guide.

- General:

  - The Modular Riser guide features mechanical interlocking rubber links with a wire mesh slide belt.

  - The Modular Riser Guide is installed in a floor slab to isolate structure from pipe borne noise and vibration.

  - The Modular riser Guide shall restrain lateral movement of the pipe and allow axial movement.

- Products:

  - Modular riser Guide shall be by Metraflex Co. Chicago, IL.

  - Mechanical interlocking elastomer links shall be selected based on installation environment.

    - Model E features EPDM links with zinc dichromate plated carbon steel hardware (used for general applications for temperatures from -40 to +250⁰ F.)

    - Model ES features EPDM links with Stainless steel hardware (used for applications in a corrosive environment, for temperatures from -40 to +250⁰ F.)

    - Model P features Nitril links with zinc dichromate plated carbon steel hardware (used for applications with exposure to hydrocarbons for temperatures from -40 to +210⁰ F.)

    - Model P features Nitril links with stainless steel hardware (used for applications in a corrosive environment and exposure to hydrocarbons for temperatures from -40 to +210⁰ F.)

    - Model HT features Silicone links with zinc dichromate plated carbon steel hardware and plates (used for high temperature applications from -40 to +400⁰ F.)

  - Wire Mesh Slide Belt shall be 304 stainless steel.

- Execution.

  - Modular Riser Guide shall be installed per manufacturer’s instructions.

  - Use manufacturers documentation to properly select the correct size and number of links.

# Text boxes

Product Specifications